## Slide 1: Streaming Telemetry
‘Not everything that can be counted counts and not everything that counts can be counted’

## Slide 2: Hidden Agenda
In this session we will:
-> Drive your motivation to kill SNMP!

## Slide 3: Motivation
How do you monitor your Network?
If this is a picture of your NOC personnel…
You may have a Finger-Defined Network.

## Slide 4: Why Change
For us, personally:
Switches logs full of messages: “%SNMP-3-RESPONSE_DELAYED: processing GetNext of entSensorType (150023 msecs)”, too many SNMP collectors
Routers: Change of default values in control-plane policies to accommodate the rate of snmp requests
Inability to fetch important data in equipment's, ie: evpn/perf-meas
Short spaced glitches where very hard to see
Plan in motion to:
-> Improve visibility to help troubleshoot = faster problem resolution

## Slide 5: “Pushing” More Data Really Does Work Better

## Slide 6: Migrating from SNMP to GRPC Dial Out Telemetry

## Slide 7: Quick reminder: SNMP framework

## Slide 8: Version TLDR: Too Long Didn’t Read
YANG Language
Defined in 2010 by RFC 6020 by Tail-f’s Martin Bjorklund, to provide a modeling language for NETCONF – expanded beyond
Human readable, easy to learn representation – compact C and Java-like syntax
Hierarchical models with reusable types and groupings
Supports definition of operations (RPCs)
Constraints and configuration validation
Well-defined version rules
How to configure
Model: Cisco-IOS-XE-interfaces-oper.yang
Xpath/Sensor: /interfaces-ios-xe-oper:interfaces/interface/interface-type

## Slide 9: Version TLDR: Too Long Didn’t Read

## Slide 10: Streaming Telemetry Stack

## Slide 11: First Things, First: Telemetry Stack
So, what is all this fuss about Streaming Telemetry…
Real-time data collection and transmission for monitoring.
Continuous and automated delivery of telemetry data.
Faster issue detection and response.
Enables historical data analysis.
Relies on efficient and reliable protocols.
Provides visibility into network and system operations.
Optimizes performance, enhances security, ensures reliability.
“Scream Stream If You Want to Go Faster”

## Slide 12: Data Model Layer
Raw data maped to a model
(YANG models: Native, OpenConfig, etc)

## Slide 13: YANG – Yet Another Next Generation
Self-contained top-level hierarchy of nodes
Import or define data types
Containers group related nodes
Lists for sequence of entries
Leaf nodes for simple data

## Slide 14: YANG – Yet Another Next Generation
Native Models
OpenConfig Models
Aaaa, and IETF too….
In the present day, a router has about 1300 Native models and 100 OpenConfig models

## Slide 15: Configuration vs Operational

## Slide 16: Where’s Wally?
A complete guide on how to find Xpath sensor path´s in the correct yang model 101:
Google it
GPT it
Yangsuite
Github
Pyang
CLI based commands

## Slide 17: Producer Layer
Time intervals definitions for the models

## Slide 18: Publication options
On-change
Periodic
Event notifications (failed login, optics fault, etc)
State and Configuration
Time based publications
Minimum interval 1s

## Slide 19: Telemetry Taxonomy
Event-Driven Telemetry
Model-Driven Telemetry
Router X
Router X
Time
100 Interfaces UP/ 0 Down
100 Interfaces UP/ 0 Down
100 Interfaces UP/ 0 Down
99 Interfaces UP/ 1 Down
99 Interfaces UP/ 1 Down
Time
100 Interfaces UP/ 0 Down
99 Interfaces UP/ 1 Down

## Slide 20: Points of Consideration - Equipment's
What sensors/instrumentation are supported?
What is max/min frequency of export?
Can it be exported by ’event’ (on-change)?
What is the most-specific ‘branch’ needed to export?
NETWORK
COLLECTOR
DATABASE
VISUALIZATION
ALERTING

## Slide 21: Exporter Layer
Encoding and transportation for the models
It’s all about the
Apey Eyes
APIs
Get it!?
gNMI
gRPC
NETCONF
RESTCONF
SNMP
CLI

## Slide 22: MDT Modes, Dial-In vs Dial-Out
Broader flexibility in transport options
No need to open ports for inbound management traffic
Anycast & Load-balancing
A single channel (config and streaming)
Listening port on the router
No MDT configuration on the router
Only gRPC/gNMI available
Dial-out
Dial-in

## Slide 23: The State of Monitoring/Operations

## Slide 24
A modern opensource high performance RPC framework
Provides push or pull methods to obtain metrics
Highly efficient on wire and with a simple service definition framework
Device to collector PUSH method is one-way and efficient
Collector to Device PULL method is like SNMP poll-response; less-efficient, but less configuration management.
Bi-directional streaming with http/2 based transport – also providing TLS support
https://grpc.io/
Transport: Google Remote Procedure Call (gRPC)

## Slide 25: Encoding Options
Compact GPB
Key-Value GPB
JSON
Encoding (or “serialization”) translates data (objects, state) into a format that can be transmitted across the network. When the receiver decodes (“de-serializes”) the data, it has an semantically identical copy of the original data.
{ "node-name: “0/RP0/CPU0”,
”process-cpu”: {
{ “total-cpu-fifteen-minute”: 5,
“total-cpu-five-minute”: 6,
“total-cpu-one-minute”: 12 }}}
1: 0/RP0/CPU0
10: 5
11: 6
12: 12
“Compact”
Faster to transfer – less data
More complex to correlate
From https://developers.google.com/protocol-buffers/
“Self-describing”
More data to transfer
“Protocol buffers are Google's language-neutral, platform-neutral, extensible mechanism for serializing structured data – think XML, but smaller, faster, and simpler.”

## Slide 26: Architecture
NETWORK
COLLECTOR
DATABASE
VISUALIZATION
ALERTING
NETWORK
COLLECTOR
DATABASE
VISUALIZATION
ALERTING
NETWORK
COLLECTOR
DATABASE
VISUALIZATION
ALERTING
Porto
Lisboa
IPCB

## Slide 27: Summary And Key Messages
We must change the way we operate networks
Automation and programmability are required this days
On board management for support, complexity is everywhere nowadays
Data Mode-driven is required for configuration, hence model-driven telemetry
YANG is the data modeling language for configuration and monitoring
Be specific with what you want to push
Use OpenConfig models, for consistency, when possible
TLDR: use gRPC, dial out, with Key Value protobuf
Use Event-driven telemetry when appropriate

## Slide 28: Analytics Layer
Data collection, processing and visualization
Notes: Coletor
Processamento (e.g não guardar dados de interfaces down, para economizar espaço)
Apresentação
Tentar comparar com SNMP sempre que possível

## Slide 29: Is the infrastructure ready?
Per Process
Load
DRAM
Utilization
Disk
Utilization
Network
Bandwidth
https://xrdocs.io/telemetry/tutorials/2018-07-10-is-your-infra-ready-for-telemetry/
Notes: Antes da implementação de um projeto de streaming telemetry, é essencial garantir que a infraestrutura cumpre com as exigências de um projeto desta dimensão
A nossa análise baseou-se num artigo chamado “Is your infra ready for telemetry?” do XRdocs
Este artigo apresenta um estudo aborda 5 métricas chave no que toca à infraestrutura, sendo elas:
  Load por processo
  Utilização de DRAM
  Utilização de Disco
  Largura de Banda

## Slide 30: Is the infrastructure ready?
~2vCPU
CPU E5-2697 v3
@2.60Hz
~1.2GB
DDR4 / 2133Mhz
~1GB
Space per hour
One Router
350k counters / 5 sec.
https://xrdocs.io/telemetry/tutorials/2018-07-10-is-your-infra-ready-for-telemetry/
Per Process
Load
DRAM
Utilization
Disk
Utilization
Network
Bandwidth
~75Mbps
~90MBps
SM1625 800GB 6G 2.5” SAS SSD
Notes: O estudo baseia-se na análise do processo de recolha e armazenamento
Os valores de referência são para a recolha de 350,000 contadores de um router a cada 5 segundos
Destaca-se principalmente o espaço em disco, que ronda 1GB por hora e estamos a falar de apenas um router
No nosso caso, a recolha de dados não deverá ser tão frequente, pelo que estamos a apontar para recolhas de 20 em 20 segundos
Contudo, temos cerca de 200 equipamentos ativos, que certamente gerará enormes volumes de dados
Será, por isso, necessário um armazenamento de dimensões consideráveis, tendo este de ser composto por SSDs, para que o acesso aos dados seja, também ele, o mais rápido possível

## Slide 31: Analytics Stack
NETWORK
Notes: O estudo mencionado refere-se a um stack de ferramentas semelhante a este
Este stack é conhecido por TIG stack e é composto pelo Telegraf, InfluxDB e Grafana.
Todas estas ferramentas têm já alguma maturidade e são bastante adotadas pela comunidade
Verificámos vários exemplos da utilização do mesmo, exatamente com o propósito de armazenamento, processamento e visualização de dados de telemetria
Uma vez que já utilizávamos InfluxDB e Grafana para a nossa camada analítica relacionada com o SNMP, fez todo o sentido adotarmos este stack

## Slide 32: Analytics Stack
NETWORK
COLLECTOR
DATABASE
VISUALIZATION
ALERTING
Notes: O estudo mencionado refere-se a um stack de ferramentas semelhante a este
Este stack é conhecido por TIG stack e é composto pelo Telegraf, InfluxDB e Grafana.
Todas estas ferramentas têm já alguma maturidade e são bastante adotadas pela comunidade
Verificámos vários exemplos da utilização do mesmo, exatamente com o propósito de armazenamento, processamento e visualização de dados de telemetria
Uma vez que já utilizávamos InfluxDB e Grafana para a nossa camada analítica relacionada com o SNMP, fez todo o sentido adotarmos este stack

## Slide 33: Analytics Stack

## Slide 34: Analytics Stack
Open-source data collection agent
Supports a wide range of input plugins for gathering data from various sources
Ideal for handling high-frequency data streams
Excels at collecting metrics from systems, sensors, and applications in real-time
Can process input data before storing it into a database
Allows the collection of metrics from multiple vendors and models
Notes: O Telegraf é um agente de recolha de dados que possui uma série de plugins de input para recolha de dados provenientes de várias fontes
Foi especialmente desenhado para fluxos de dados de elevada frequência, quer sejam de métricas de sistemas, sensores ou aplicações em tempo real
Permite a configuração de um processo de recolha, processamento e escrita dos dados (i.e. semelhante a um ETL) apenas via ficheiros de configuração
Em termos de processamento, podemos aplicar transformações e filtros, que podem ser úteis para economizar espaço na base de dados (e.g. guardar apenas os dados de interfaces de rede cujo estado não esteja down)
O estudo que analisámos utilizava o CISCO Network Telemetry Pipeline como alternativa, mas optámos por não o usar, por ser proprietário da CISCO
Assim sendo, utilizando o Telegraf, temos a possibilidade de recolher métricas de vários equipamentos independentemente do fabricante ou modelo

## Slide 35: Analytics Stack

## Slide 36: Analytics Stack
Time series database that specializes in storing and querying time-stamped data
Handles high ingest rates and frequent data updates associated with streaming telemetry
Flexible schema that enables adding and modifying measurements on the fly without disrupting data ingestion
Using version 2 is strongly recommended, as its new query language is much more versatile
Notes: A InfluxDB é uma base de dados especializada em séries temporais
Tal como o Telegraf, é capaz de lidar com fluxos de dados de elevada frequência, quer a nível de inserção, quer de atualização, o que a torna muito útil no que toca ao armazenamento de dados de telemetria
Outro aspeto que ajuda a lidar com dados de telemetria é a flexibilidade do modelo de dados da InfluxDB, que permite que sejam adicionadas ou modificadas métricas sem que haja disrupção da ingestão de dados, o que é útil visto que podemos adicionar novas métricas
Atualmente utilizamos a versão 1 da InfluxDB, o que tem se mostrado problemático, visto que a linguagem de querying InfluxQL é algo limitada
Por exemplo, em InfluxQL, não é possível aplicar operações a strings, como “split”, “replace”, “length”, etc.
Também não é possível agrupar dados por campo, apenas por chave, o que por vezes é útil dado os valores recolhidos da telemetria
Desta feita, recomendamos o uso da versão 2 da InfluxDB, uma vez que introduz a linguagem Flux, que oferece uma série de novas funcionalidades e que vêm resolver os problemas com que nos deparámos e outros mais
De notar que foram consideradas outras bases de dados, como MongoDB, ou TimescaleDB, mas a maturidade, versatilidade e capacidade de lidar com séries de dados temporais da InfluxDB, aliada ao facto de já estarmos a utilizá-la para dados de SNMP, fizeram com que optássemos pela mesma

## Slide 37: Analytics Stack

## Slide 38: Analytics Stack
Data visualization and analytics tool that integrates seamlessly with InfluxDB
Provides a user-friendly interface for creating interactive dashboards and exploring time series data
Allows monitoring, analyzing, and presenting streaming telemetry data effectively
Notes: O Grafana é uma ferramenta para visualização de dados que integra diretamente com a InfluxDB, embora também com outros tipos de fontes de dados
Permite a criação de dashboards interativos focados em séries de dados temporais, daí ser
Permite monitorizar, analisar e apresentar dados de telemetria de forma eficiente

## Slide 39: Visualization

## Slide 40: Use Case: Perf-Meas

## Slide 41: Segment Routing Stack

## Slide 42: Performance Measurement
Query's sent every 1s (default 3s)
Probes completed after 10 query's
Timestamps added in hardware
PM Query format: RFC 5357 (TWAMP) or RFC 6374 (MPLS)
Extracted values: Max, Min, Average, Variance, Query's sent/received
1
2
PM Query Packet
PM Response Packet
TX Timestamp T1
TX Timestamp T4
TX Timestamp T2
TX Timestamp T3
Measurement mode:
One-Way (T2-T1)
Two-Way (T4-T1)
Loopback
Probes type:
Interface
Endpoint
SR-TE

## Slide 43: Performance Measurement

## Slide 44: Data Pushed with Streaming Telemetry

## Slide 45: Lisbon-Porto Litoral vs Beiras

## Slide 46: Last Mile per Hop Data: O’Really?

## Slide 47: But Wait… There’s more o.O
If SR-TE handles Minimum delay (propagation delay):
Minimum delay provides the propagation delay (Fiber length / speed of light)
A property of the topology (with awareness of DWDM circuit change)
SR-TE (SR Policy or Flex-Algo) can optimize on min delay
Stay tuned for 2024!
And SR IGP Flexible Algorithms (Flex-Algo) can:
Make a algorithm defined by the operator, on a per-deployment basis
Flex-Algo K is then defined as:
  The minimization of a specified metric: IGP, TE or delay
So we can have a dual planar network!!
Algo 0
Algo 128

## Slide 48: Try It Yourself
Demo

## Slide 49: Try it! No, Really Try it!!
TIG MDT Docker Container
https://github.com/DataKnox/Cisco-MDT-TIG-Docker
https://github.com/CiscoDevNet/yangsuite
Separate Container
Telegraf
InfluxDB
Grafana
Collector
Storage
Visualization
gRPC Server Port 57500
gNMI Configuration
Port 8086
HTTP Port 3000
Yang Suite
HTTP Port 8480

## Slide 50
FCT|FCCN
Network Services Area
João Silva joao.silva@fccn.pt
Gonçalo Lopes goncalo.lopes@fccn.pt
Over and Out!
Thank You!